## Slide 1: Two-Tiered City Logistics Modelling Demand Uncertainty in Tactical Planning
Teodor Gabriel Crainic
TeodorGabriel.Crainic@CIRRELT.ca
Colloque Logistique Urbaine et Interdisciplinarité, Paris
Le 27 novembre 2014

## Slide 2: City Logistics Ideas
“New” organizational strategies/models
  Reduce & control freight vehicle flows & types
  Improve efficiency of freight transportation
    Higher loads, less empty vehicle-km
  Reduce environmental footprint & congestion & interference with people impact
Without penalizing its economic activities
To foster an efficient transportation system
To make the city a better place to experience: live, work, visit, move within and through …
Work on demand & supply sides + behaviour, policy, regulation, law, …

## Slide 3: Move Freight Differently, “Out of the Way”
Underground automated systems: new supply systems
  Conveyor belts or adapted vehicles on particular infrastructure
  Particular packing
  Loading/unloading stations
  Huge investments required
Night deliveries: Move the demand out in time
  Successful pilot in New York city – much interest elsewhere
  Requires particular city regulations
  Does not necessarily decrease number of vehicles

## Slide 4: Move Freight Differently (2)
Most actual systems, past projects and proposals are based somehow on the principle of
Consolidation and coordination
  Coordination of shippers and carriers (& consignees)
  Consolidation of several shipments of different shippers & carriers into, and delivery by the same (improved, more energy efficient, “green”) vehicle
Makes use of one or a series of terminals
  Consolidation facilities, Urban / city distribution / logistics centers, of various sizes and roles

## Slide 5: The City Logistics (Supply) Fundamental Idea
An integrated logistics system =
  Shippers, shipments
  Carriers (all modes including passenger and interurban, e.g., rail, navigation), vehicles
  Service providers, consignees/customers, …
Optimize this logistics system
“Public system” view (not ownership!) operated as best fits the local culture, laws and regulations

## Slide 6: Single-Tier Single-CDC City Logistics
Customer
zone
Urban vehicle
City
Distribution
Center

## Slide 7: City Logistics for Large or Sensitive Urban Areas
Most display a two-tier structure
  Loads consolidated at CDC into “large” vehicles
  Moved to CDC-like facilities – satellites – “close” to customers
  Transferred to “small” vehicles appropriate for city center
  Delivered to final destinations

## Slide 8: Multi-Tiered City Logistics
S
S
S
S
S
S
P
P
P
Center 1
Center 2
Origin-node
Airport
Railway station
Navigation Terminals
Platforms
Depots
Satellites
S
Railway station

## Slide 9: Two-Tier City Logistics
CDC
Satellite CDC

## Slide 10: Two-Tier City Logistics
City freighter - route
Urban vehicle - route
Empty vehicle

## Slide 11: 2T-CL with Rail & Transit (Public Transport)
Navigation
Long-Haul Trucks
Rail
City Freighter
Urban Vehicle
Satellite Crossdock
Customer
Distribution center
City route
City Distribution Center

## Slide 12: City Logistics for Large Cities
Several not necessarily integrated sub-systems
Many have access to some public infrastructure (light rail lines, parking lots, …) even for private initiatives
A few initiatives to use dynamically available transportation & storage capacity
An implicit idea: Disconnect the actual mean of transportation / delivery from the carrier/shipper/3PL originally contracted
Private inititive implementing CL operating principles
Multimodal systems that aim for intermodality

## Slide 13: Modular & Standard Physical Internet -Containers

## Slide 14: Interconnected, Multi-tiered City Logistics
Ship
Long-distance vehicle
Train
City freighter
Plane
Bicycle
Urban vehicle
Urban hub

## Slide 15: Challenges & Opportunities
CL = complex consolidation-based transport system
  Multiple “layers”, facilities, fleets, modes
  Time restrictions, dependencies, synchronization
Goal of sustainable efficiency for stakeholders & city
  Operations Research & Transportation Science
  “New” problems  New models, algorithms, instruments
  Methods for the system and its components
    Appropriate for the decision-level concerned

## Slide 16: Challenges & Opportunities (2)
Culturally and socially-aware organization and business models, e.g.,
Cultural (government ↔ people & business, business models, taxation, etc.) impact and need for somewhat tailored solutions
Stakeholder behaviour modelling
Demand identification and modelling
Partnerships & collaborations → Supply modelling
Public policy
Materials (“boxes”), law, regulation, land use, …

## Slide 17: An illustration of O.R. development: Uncertainty and tactical planning Nicoletta Ricciardi (Sapienza U. di Roma) Walter Rei (UQAM) Fausto Errico (CIRRELT)

## Slide 18: Tactical (Medium-term) Planning
season
day
Tactical planning = Plan regular operations, based on a (point) forecast, for efficient resource allocation & utilization, customer satisfaction, profitable operations
Day-to-day situation generally different from forecast
X
Build the plan
Adjust the plan
X

## Slide 19: Accounting for Uncertainty
season
day
Tactical medium-term planning accounting for uncertainty = Integrate into the tactical planning model/method the possible “adjustments” and their costs
X
Build a more flexible and robust plan
Adjust the plan “less”
X
System data Forecast demand
Observed demand

## Slide 20: Sources of Uncertainty in City Logistics
Time
  Work at facilities & service at customers
  Travel through the city
Demand (regularity of activities within customer zones)
  Volume (including no show; volume = 0)
  Unexpected
Rare but predictable events (e.g., vehicle or infrastructure incidents)
Rare, “catastrophic” events

## Slide 21: Demand Uncertainty & Planning
Robust plans (flexible operations) versus managerial concerns
Build a season plan based on available/forecast data
Each “day”, once the uncertain demand data is resolved
  Keep part/most of the plan
    External and satellite facility utilization
    Urban-vehicle service network
  Adjust using a recourse policy
    Routing city freighters and extra vehicles
Two-stage modelling

## Slide 22: Two-Stage Modelling Framework
Two-stage recourse formulation
First stage
  Selection of first-tier services (& departure times)
  Allocation of customers to services & satellites
Second stage
  Routing of second-tier city freighters
  Service adjustment (eventually)
  Customer-to-satellite allocation (eventually)
  Calling on extra vehicles (when required)

## Slide 23: Two-Stage Stochastic Programming
A priori optimization
First-stage decisions: the a priori plan x
: Realization of demand for
: Cost of “optimal” operation plan using the a priori plan for demand given a recourse policy RP

## Slide 24: Problem Elements: Facilities & Customers
d
External zone
e
Satellite
Customer demand

## Slide 25: Scheduled Urban-Vehicle Services
r’: t(r’)=t
r: t(r)=t+1
Decision: Which
service to run? (When?)
e
s
(r)  {1,0}
r’: t(r’)=t; (r)={z}

## Slide 26: City-Freighter Work Segment & Assignment
st
s’t+
c4
gt-
g’t++
e’t’
e’’’t’’’
e’’t’’
c2
c3
c4
c1
c5
c6
c7
c8
c8
c3
c2
c1
c5
c7
c6
(h) {1,0}
Decision: Which
c-f work assignment
to operate?

## Slide 27: Demand Itineraries
m:{e,r(m),t(m) < t(r),
z(m)=z(m) (r(m)), (p(d)), l(h(m)), c(d)}
d
z’
z
Select itinerary to deliver cargo on time: (m)  {1,0}
e
d: e,c,p,t,[a,b],vol

## Slide 28: First Stage
Information considered
  System data
  Estimation of future demand
Defining an a priori plan
  Aggregated service network design model with approximate routing costs (Tr. Sc. 2009)
Decision variables

## Slide 29: First Stage Formulation
Generalized cost first-tier services
Generalized cost second-tier
work assignments – forecast demand
Recourse cost
U. Vehicle capacity Linking
Single itinerary
Satellite capacity U. Vehicles
C. Freighters

## Slide 30: First Stage Output – The Plan

## Slide 31: Second Stage – Observing the Demand
All demands  Forecasts
  Determine routing = Synchronized, scheduled, multi-depot, multiple-tour, heterogeneous VRPTW
  Attempt to improve system response = Apply a recourse policy + routing
Adjust plan + routing, otherwise
Straightforward to determine which customers need extra capacity to be serviced

## Slide 32: 2nd Stage Recourse Policies
Routing (R)
Routing & possible customer re-assignment (RA)
Service Dispatch and Routing (SR)
Service Dispatch, Routing & possible customer re-assignment (SRA)
Increased latitude in the recourse actions
Extra city freighters with high cost for the demand that cannot be moved by regular vehicles
  A single city-freighter fleet to service the “regular” and the “extra” demand
  Direct-shipment policy

## Slide 33: 3-Leg City Freighter Work Segment
Direct shipment

## Slide 34: 2nd Stage Routing Recourse
Keep
  Selected first-tier services (routes and schedules)
  Customer-to-satellite assignments  Bounds on second-tier vehicle departures at each rendez-vous point (satellite, period)
Optimize the routing & demand itineraries

## Slide 35: 2nd Stage Routing Recourse
Keep
  Selected first-tier services (routes and schedules)
  Customer-to-satellite assignments  Bounds on second-tier vehicle departures at each rendez-vous point (satellite, period)
Optimize the routing & demand itineraries

## Slide 36: Formulation

## Slide 37: 2nd Stage Route & Reassign Recourse
Keep
  Selected first-tier services (routes and schedules)
Relax the customer-to-satellite rendez-vous assignments
Optimize the routing & demand itineraries without pre-assignment of customers to satellites
Same formulation, larger set of itineraries, simpler stochastic formulation

## Slide 38: 2nd Stage Service Dispatch and Routing Recourse
Keep
  Selected first-tier services (routes and schedules)
  Customer demands to be served from each (satellite, period) point
Identify satellite opportunity windows and urban-vehicle compatible services

## Slide 39: Output of Service Network Design
zt
i
j
k
et’

## Slide 40: Opportunity Windows and Compatible Services
zt
i
j
k
et’

## Slide 41: 2nd Stage Service Dispatch and Routing Recourse
Optimize the restricted selection of services, the routing of regular and extra city freighters & demand itineraries: restricted tactical model
  With and without fixed customer-to-rendez-point assignment

## Slide 42: 2nd Stage Service Dispatch and Routing Recourse
Optimize the restricted selection of services, the routing of regular and extra city freighters & demand itineraries: restricted tactical model
With and without fixed customer-to-rendez-point assignment

## Slide 43: Formulation SR Recourse

## Slide 44: Experimental Study of Recourse Alternatives
System performance & management issues
Monte Carlo-like simulation
  Not an evaluation of the value of stochastic model

## Slide 45: Experimental Setup
The four recourse strategies
No tactical plan but daily plan = “the day before”
A simplified setting: single product & vehicle type, fixed travel times, no split
Data sets randomly generated – “small” dimensions (including with realistic geographical settings)
  1-2 external zones, 2-3 satellites, 15 & 25 customer zones, 6 periods of 25 minutes (2.5 hours)
  2 demand-size distributions, 2 prediction values

## Slide 46: Evaluation Procedure

## Slide 47: The Hierarchical Decomposition
Urban-vehicle service design
City-Freighter routing
Customer-to-satellite assignment Approximate cost of serving each customer from its satellite
Selected services
Custer demands at satellite-period
City-freighter work assignments

## Slide 48: Experimental Setup (2)
Analyses based on
  Traffic intensity: numbers of vehicles, vehicle-km
  Vehicle (capacity) utilization
  System cost
  Impact & social cost
  Managerial concerns

## Slide 49: Cost Analysis
No-planning = Lower bound on costs & no direct deliveries (extra vehicles); Management (e.g., labor)?
Cost of planning ≈15% and but extra vehicles
More flexibility = less direct services (60%, lower variance) & costs (2% - 3.5%)
Direct services: ↑nb. Customers, ↓nb. of CDC
Do not use the “average” forecast

## Slide 50: Route Length Analysis
More flexibility = shorter city-freighter routes (4,8%) and less empty travel (6%)
Higher empty travel with # of customers
Lower empty travel with # of external zones / satellites
Modifying – sliding – the urban-vehicle departures appears beneficial

## Slide 51: Vehicle Capacity Utilization
No planning = few more vehicles 1st level, less on 2nd
Planning yields very good loading factors
More flexibility yields better vehicle loadings (≈ 15%)
Most city freighters operate a single leg, a few two  Need to investigate “waiting” strategies (synchronization is hard)

## Slide 52: Satellite Utilization
System appears stable
Increasing flexibility, increases the “volatility” of using the satellites
Trade off to find between operation flexibility and management concerns
Need of ITS
Standard deviations

## Slide 53: Conclusions and Perspectives
Flexibility in adjusting the plan is beneficial on all counts: costs, km performed, capacity utilization …
It might come with higher requirements for management (& labor relations and work rules) flexibility
Needs advanced IT and decision-support systems
NOW:
Address the stochastic models (and the deterministic ;-)
Large dimensions
City Logistics systems design, policies, financing, …